## Slide 1: LoRaWAN Simulator Architecture and Data Flow
End-to-end Simulation of LoRaWAN OTAA Device, UDP Gateway, and The Things Stack

## Slide 2: Agenda
Introduction to LoRaWAN Simulator
Simulator Architecture
Data Flow: Uplink & Downlink
OTAA Join Flow
Join-Accept & Key Derivation
End-to-End Example
Future Enhancements

## Slide 3: Introduction
Purpose: Simulate LoRaWAN communication without radio hardware.
Key Components:
  Simulated End Device (OTAA, Uplink Payloads)
  Simulated UDP Gateway (Semtech UDP Protocol)
  The Things Stack (Network Server)
  Application Layer (MQTT/Webhooks)

## Slide 4
Simulator Architecture Overview
Simulated End Device
(OTAA, Uplinks)
UDP Gateway Simulator
(Semtech UDP)
The Things Stack (TTS)
(Join, MIC, Routing)
Application Layer
(MQTT/Webhooks)
Device → UDP Gateway → TTS → Application Layer. End-to-end simulation without radio hardware.

## Slide 5: Component Details
Simulated Device:
  Performs OTAA and encrypted uplinks.
  Derives session keys dynamically (NwkSKey, AppSKey).
UDP Gateway:
  Implements Semtech UDP protocol.
  Handles PUSH_DATA/PULL_DATA messages to TTS.
The Things Stack:
  Handles join requests, MIC validation, and routing to apps.

## Slide 6: Data Flow: Uplink & Downlink
Uplink Path:
  Device creates LoRaWAN frame.
  Gateway forwards via Semtech UDP to TTS.
  TTS validates MIC and decrypts payload.
Downlink Path:
  App sends message to TTS.
  TTS schedules RX1/RX2 window.
  Gateway transmits downlink to device.

## Slide 7
Data Flow Diagram
Simulated End Device
(OTAA, Uplinks)
UDP Gateway Simulator
(Semtech UDP)
The Things Stack (TTS)
(Join, MIC, Routing)
Application Layer
(MQTT/Webhooks)
Shows bidirectional flow between Device, Gateway, TTS, and Application.

## Slide 8: OTAA Join Flow (Step-by-Step)
1. Device builds Join-Request (AppEUI, DevEUI, DevNonce, MIC).
2. Gateway forwards to TTS.
3. TTS authenticates and allocates DevAddr, NetID.
4. TTS creates Join-Accept, encrypts with AppKey.
5. Gateway transmits Join-Accept in RX window.
6. Device decrypts Join-Accept, derives NwkSKey & AppSKey.
7. Device starts encrypted uplinks.

## Slide 9: Join-Accept Packet Breakdown
Fields:
  JoinNonce (AppNonce), NetID, DevAddr, DLSettings, RxDelay, CFList.
Security:
  Encrypted using AES-128 ECB with AppKey.
  Device decrypts before key derivation.
Key Derivation:
  NwkSKey = aes128(AppKey, 0x01 | JoinNonce | NetID | DevNonce)
  AppSKey = aes128(AppKey, 0x02 | JoinNonce | NetID | DevNonce)

## Slide 10: End-to-End Example
Simulated device sends Join-Request to Gateway.
Gateway → TTS → Join-Accept sent back.
Device derives keys and sends encrypted temperature data.
TTS decodes payload and forwards via MQTT/Webhooks.

## Slide 11: Simulator Data Flow Summary
Protocols: UDP, AES-128, MQTT.
Security: End-to-end encryption with AppKey.
Scalable for multiple gateways/devices.
Integrates seamlessly with TTS cloud or local setup.

## Slide 12: Future Enhancements
Support multi-gateway and multi-node simulation.
Add ADR logic, Class B/C downlinks.
Integrate LoRa Basics Station (WebSocket).
Add Grafana dashboard visualization.

## Slide 13: Conclusion
LoRaWAN Simulator enables testing without radio hardware.
Validates join, encryption, and payload routing.
Easily extensible for advanced IoT environments.