## Slide 1: LoRaWAN Simulator
A Complete Virtual Environment for LoRaWAN Testing and Development
Author: [Your Name]
Organization: [Institute / Company]
Date: [Insert Date]

## Slide 2: Introduction to LoRaWAN
• LoRaWAN (Long Range Wide Area Network) is a low-power wireless protocol for IoT devices.
• Designed for long-range communication, low power, and secure data transfer.
• Typical architecture includes End Devices, Gateways, and Network Servers.

## Slide 3: What is a LoRaWAN Simulator?
• A LoRaWAN Simulator replicates real-world LoRaWAN communication in software.
• Simulates:
- End Devices (sensors)
- Gateways
- Network Servers (e.g., The Things Stack)
• No need for physical LoRa hardware.

## Slide 4: Architecture of the LoRaWAN Simulator
Components:
1. Simulated End Device – Generates data, performs OTAA join.
2. Simulated Gateway – Forwards packets using Semtech UDP.
3. Network Server – Handles join requests and uplinks.
Flow: End Device → Gateway → Network Server (TTS).

## Slide 5: System Flow Diagram
1. Device sends Join Request (OTAA)
2. Gateway forwards to TTS
3. TTS returns Join Accept
4. Device derives session keys (NwkSKey, AppSKey)
5. Device sends encrypted uplinks
6. Gateway forwards to TTS

## Slide 6: Benefits of the LoRaWAN Simulator
✅ Hardware Independent: No LoRa modules needed.
⚙️ Faster Testing: Test joins and uplinks quickly.
🔐 Security Validation: Verify encryption and MIC.
📡 Protocol Learning: Great for education.
🧩 Customizable: Modify payloads and timing.

## Slide 7: Small Use Case Example
Use Case: IoT Temperature Monitoring Simulation
• Device sends temperature every 10s.
• Gateway forwards via UDP to TTS.
• Data visible on TTS/MQTT.
• Validates encryption and timing.

## Slide 8: Key Features Implemented
• OTAA Join (AppEUI, DevEUI, AppKey)
• MIC verification and AES128 encryption
• UDP packet forwarding
• Periodic uplinks
• Multi-device scalability

## Slide 9: Technology Stack
• Language: Python
• Protocols: LoRaWAN 1.0.3, Semtech UDP 2.3
• Backend: The Things Stack (Cloud/Local)
• Environment: Docker/VMs
• Libraries: socket, struct, Crypto, time, json

## Slide 10: Benefits to Developers & Researchers
• Prototype LoRaWAN apps quickly.
• Test large-scale virtual networks.
• Learn encryption & key management.
• Integrate with cloud analytics.

## Slide 11: Future Enhancements
• Support Class B/C devices.
• Web-based dashboard.
• Multi-region frequency support.
• AI-based network optimization.

## Slide 12: Summary
• LoRaWAN Simulator = full virtual LoRaWAN stack.
• Enables testing, dev, and education without hardware.
• Extendable for research and IoT projects.

## Slide 13: Thank You!
Contact: [Your Email]
GitHub: [Simulator Repo]
Website: [if available]

## Slide 14
Simulator Architecture Overview
Simulated End Device (OTAA, Uplinks)
Simulated UDP Gateway (Semtech UDP)
Network Server (TTS) (Join, MIC, Routing)
App Integrations (MQTT/Webhooks)
End-to-end simulator architecture with horizontal data path. Devices talk LoRaWAN → UDP gateway forwards packets → TTS processes joins/uplinks → App layer consumes via MQTT/Webhooks.

## Slide 15: Data Flow: Uplink & Downlink
Uplink Path
Device creates LoRaWAN frame (MHDR, FHDR, FPort, FRMPayload, MIC)
  Frame is transmitted → captured by Simulated UDP Gateway
  Gateway wraps into Semtech UDP packet and forwards to TTS
  TTS validates MIC, decrypts (if applicable), routes to application
Downlink Path
Application enqueues downlink via TTS (optional ACKs/confirmed)
  TTS schedules RX1/RX2; hands packet to UDP Gateway
  Gateway transmits to device in the appropriate RX window
  Device processes downlink (MAC commands / App payload)
Security
MIC: AES-CMAC with NwkSKey (LoRaWAN 1.0.x)
  Payload encryption: AES-128 with AppSKey (FPort ≥ 1)

## Slide 16: OTAA Join Flow (LoRaWAN 1.0.3)
1) Join-Request (DevEUI, AppEUI/JoinEUI, DevNonce, MIC)
2) Gateway forwards Join-Request via Semtech UDP to TTS
3) TTS authenticates, allocates DevAddr, generates session context
4) Join-Accept created (JoinNonce/AppNonce, NetID, DevAddr, DLSettings, RxDelay, CFList)
5) Join-Accept is encrypted with AppKey and sent via Gateway
6) Device derives NwkSKey & AppSKey from AppKey + Join parameters
7) Device switches to activated state and starts encrypted uplinks

## Slide 17: Join-Accept Details (LoRaWAN 1.0.x)
Fields
JoinNonce (a.k.a. AppNonce): Random from Network Server
  NetID: Network identifier
  DevAddr: Assigned device address
  DLSettings: RX1DRoffset & RX2 data rate
  RxDelay: Delay to RX1 window (seconds)
  CFList: Optional channel list for region
Security & Derivations
Join-Accept is encrypted with AES-128 using AppKey
  NwkSKey = aes128(AppKey, 0x01 | JoinNonce | NetID | DevNonce)
  AppSKey = aes128(AppKey, 0x02 | JoinNonce | NetID | DevNonce)
Timing
Device listens RX1/RX2 after Join-Request
  Gateway must transmit within TTS-scheduled window